CAD Conventions

Overview
To maintain homogeneity across all module designs, we should attempt to maintain a common structure across all FreeCAD files. This document hopes to formalise names and hierarchies.

Module Scope
Minimum Viable Module Set	General: / - [done] [bom] [drw] Base mat / - [done] [bom] [drw] Post holders / - [done] [bom] [drw] Posts / - [done] [bom] Pedestals / - [done] [bom] Clamping fork / Mounts: / - [done] [bom] [drw] V-groove lens/laser mount / - [done] [bom] Filter/mirror mount / - [done] [bom] Prism platform / Cage: / - [done] [bom] Poles / - [done] [bom] Post mount / - [done] [bom] Structural tie
Preferred Module Set	General: / - [done] [bom] [drw] Cylindrical object mount / - [done] [bom] XY translation lens holder / - [done] [bom] [drw] XY rotation lens holder / Cage: / - [done] [bom] 90° Junction / - [done] [bom] Cross junction / - [done] [bom] Side branch mount / - [done] [bom] Spiral lens holder / - [done] [bom] XY rotation lens holder / - [done] [bom] XY translation lens holder / - [done] [bom] Pole-to-pole tie
Extended Module Set	General: / - Motorised rotating filter mount / - [done] [bom] Iris / - Optical rail / Cage: / - Shearing interferometer casing / - Adapters for competing cage systems

Document Hierarchy
All geometry (such as Bodies created with Part Design workbench) should be encapsulated within a Part object. Multiple parts can be defined within the same document, but if they are meant to be separate objects, they should be enclosed different Parts.
Parts can be created with a button present in both the Part Design and Part workbenches.

File Naming Conventions
File names should be lower case and must not contain spaces. Descriptors filenames must be separated with dashes.
General format:
<name>_<name>-<descriptor>
Examples:
junction-cross
Junction-corner
post_holder-60mm
post_holder-70mm

Part Naming Conventions
Parts should be given a friendly display name that can contain spaces and capitals.
All geometry within the Part (Bodies, primitives, etc.) should be named in snake_case. The naming of Part Design features and sketches does not matter provided they are descriptive.
Parameter Aliasing
Where possible, dimensions should be referenced from a spreadsheet rather than hard-coded into the sketch or feature. This allows the creation of multiple linked copies of parts whose parameters can be altered independently.
Caution: When creating parametric models, values should be inherited from a single spreadsheet in a central file to avoid dependency loops. For example, if models FILE1 and FILE2 require a common value, they should both inherit it from a spreadsheet in FILE3. FILE1 and FILE2 must not reference each other directly.

Alias Naming Conventions
FreeCAD Parameter aliases start with a sequence that indicates its type followed by its name. All characters should be lower case, and words should be separated by underscores (snake_case).
<parameter key>_<name>
For example, the inner radius of a shaft could be called ri_shaft.
Key	Value
w	Width
h	Height
t	Thickness
wt	Wall Thickness
l	Length
[dr]i	Inner radius/diameter
[dr]o	Outer radius/diameter
[dr]m	Major radius/diameter
[dr]mi	Minor radius/diameter
a	Angle
pt	Pitch
off	Offset
c	Clearance

Configuration Tables
Configuration tables allow parts to be switched between multiple sets of parameters defined in a spreadsheet. This is useful for creating parts which follow the same pattern but have altered dimensions.
Tutorials:
https://www.youtube.com/watch?v=D0f7bkNGAOg&t=346s
https://www.youtube.com/watch?v=nAmwGUuvnjs

## General Design Features

FreeCAD Topological Naming Problem
A major issue in FreeCAD is that the creation of new geometry can cause geometry that depends on it to break. This can result in fillets on the wrong edges, sketches attached to curves and all sorts of weird things.
More information, including how to avoid the issue: https://wiki.freecadweb.org/Topological_naming_problem
Alternatively, the Linkstage3 branch of FreeCAD (maintained by Realthunder) can be used. This includes automatic and backwards-compatible solutions for the topological naming problem that work in most cases:
https://github.com/realthunder/FreeCAD/releases

Fillets
It is recommended to replace sharp edges with fillets to avoid stress concentrations.
For visual consistency across all parts, try to make fillets with lengths of 1mm or 0.5mm.

Design for 3D Printing
To be printed effectively a part must have:
- Good adhesion with the platform.
- No significant overhangs
Parts should have a flat surface that will be in contact with the base during manufacture. Overhangs should be avoided.

Threads
For maximum accessibility, built-in threads below M5 are to be avoided in favour of metal thread inserts. This removes the requirement for a very high-quality 3D printer which some users will have access to. If a built-in thread is required, it can be generated with the Hole feature in the Part Design workbench.
A question about 3D-printing threads:
https://3dprinting.stackexchange.com/questions/3160/printing-screws-is-the-output-usable-m3-or-m4

Drawings
Drawings must be made on the TechDraw workbench. To start a new drawing, click on ‘Insert Page Using Template’ and select ‘A?_Landscape_ISO7200_Pep.svg’. The title block can be filled out by double-clicking on the green highlighted areas. Fields in the title block should be full capitals (I think).
The ‘Insert Projection Group’ button can be used to create first and third angle projections.
The style of dimension arrows can be changed in the ‘Drawing Style’ dropdown in the task dialogue. ISO Referencing may be clearer than the default style.